Review of Hydraulic Stimulation Technology

F. Rummel, MeSy GmbH Bochum

Although explosives, acidizing and other methods have long been used in oil and gas well treatment, high pressure hydraulic stimulation was first time successfully introduced in the Hugoton Oil Field in Kansas by the Stanolind Oil & Gas Company (later on Pan American Petroleum Company) in 1948 ( Clark, 1949). The technique was originally named Hydrafrac method. 16 years later more than 400.000 hydraulic fracturing jobs have been performed in the free world. Early developments focussed on technological aspects like pumping capacities, hydraulic fluid viscosities and pumping rates, and proppant materials. Hubbert & Willis (1957) were the first to demonstrate conclusively the influence of tectonic stress to fracture orientation. The mathematical concepts based on Kirsch (1898), Sneddon (1946) or Barenblatt (1962) were developed by Christianovich et al. (1959), Perkins & Kern (1961), Howard & Fast (1957), or Geertsma & de Klerk (1968). Fracture mechanics approaches to hydraulic fracturing were suggested by Aboud-Sayed et al. (1978), Rummel (1987), or Rummel & Hansen (1989). The powerful numerical simulator FRACPRO (RES 1991) is available commercially since app. 1990. A summary of oil and gas reservoir stimulation technology is given by Economides & Nolte (1987). For geothermal energy exploitation from HDR-systems hydraulic fracturing was first applied within the LASL HDR project in 1975 ff (e.g. Burns 1990). The hydrofrac technique was experimentally investigated in the laboratory by Haimson (1968) and in-situ within the Falkenberg granite shallow geothermal frac project (Kappelmeyer & Rummel (1987), in the shallow French HDR project at Le Mayet de Montagne (Cornet 1988) or in the Cornwall granite HDR project at about 2.5 km depth (Batchelor 1983). At Soultz-sous-Forêts almost 40 large-scale hydraulic stimulation experiments were carried out since 1988 which confirmed the concept of stimulation of pre-existing fractures for the creation of a large scale heat exchanger at depth (e.g. Baria et al. 1999). In this context hydraulic stimulation experiments as e. g. carried out in 9 km deep KTB borehole to induce microseismicity should be mentioned (Zoback & Harjes, 1997). Last not least the hydraulic stimulation of dry water wells may become increasingly important for sustainable water supply in many areas (Rummel 1997, Klee & Rummel (2005). The development of intelligent stimulation techniques and their physical understanding still is in demand for economic methane production from impermeable deep coal beds or for waste disposal into artificial fractures at great depth.

References to

Review of Hydraulic Stimulation Technology presented by F. Rummel

Aboud-Sayed AS, Brechtel CE, Clifton RJ (1978): In-situ stress determination by hydrofracturing: a fracture mechanics approach. JGR, 83, 2851-2862.

Baria R, Baumgärtner J, Rummel F, Pine RJ, Sato Y (1999): HDR/HWR reservoirs: concepts, understanding and creation. Geothermics, 28, 533-552, Pergamon.

Barenblatt GI (1962): The mathematical theory of equilibrium cracks in brittle fracture. Adv. Appl. Mechanics, 7, 55-129.

Batchelor AS (1983): Hot Dry Rock reservoir stimulation in the UK. Proc. 3rd Int. EC Seminar on Geoth. Energy, 681-711, Munich Nov. 1983.

Burns KL (1990): Hot Dry Rock Research – A compendium of publications Oct. 89 -Sept. 90, Los Alamos Nat. Lab. 1990 Fiscal year Report.

Christianovich SA, Zheltov YP, Barenblatt GI, Maximovich GK (1959): Theoretical principles of hydraulic fracturing of oil strata. Proc. 5th World Petr. Congr., New York, Section II 23, 289-296.

Clark, JB (1949): Hydrafrac process for well treatment. Div. Production, Am. Petr. Inst., paper 826-20-A, Spring Meeting Eastern District, Pennsylvania; Trans. AIME, 186, 1-3.

Cornet FH (1988): Projet Mayet de Montagne - etude in-situ de la perculation force d'eau en milieu granitique. Final Project Report, CEE-DGXII, AFME, CNRS.

Economides MJ, Nolte KG (1987): Reservoir stimulation. Schlumberger Educational Services Houston, SMP-7018.

Geertsma J, de Klerk F (1958): A rapid method of predicting width and extent of hydraulically induced fractures. J. Petrol. Techn., 21, 1571-1581.

Haimson B (1968): Hydraulic fracturing in porous and nonporous rock and its potential for determining in-situ stresses at great depth. PhD-thesis, Univ. Minnesota.

Howard GC, Fast CR (1957) Optimum fluid characteristics for fracture extension. Drilling & Production Practise, 261 ff.

Hubbert KH, Willis DG (1957): Mechanics of hydraulic fracturing. Trans. AIME, Vol. 210, 153-168.

Kappelmeyer O, Rummel F (1987): Terrestrial heat from impervious rocks – investigations in the Falkenberg granite massif. Geol. Jahrbuch, Reihe E/H 39, Schweizerbart Stuttgart.

Kirsch G (1898): Die Theorie der Elastizität und die Bedürfnisse der Festigkeitslehre Zeitschr. VDI, 42/29, 797-807.

Klee G. Rummel F (2005): Sustainable development of groundwater from hard rock formations. In: Rock Mech. with Emphasis on Stress (ed. Rummel), 223-234, Balkema.

Narashimhan TN (1987): Hydrodynamics of a vertical hydraulic fracture. Rep. Lawr. Berkeley Lab., Earth Sci. Div..

Perkins TK, Kern LR (1961): Width of hydraulic fractures. J. Petr. Techn., 937-949; Trans. AIME, 222 ff.

RES Resources Engineering Systems: Mechanics of fracturing and petroleum production. Seminar Hand-Out, Munich, June 1991.

Rummel F (1987): Fracture mechanics approach to hydraulic fracturing stress measurements. In: Fracture Mechanics of Rock (ed. Atkinson), 6, 217-239.

Rummel F (1997): Stimulation einer Mineralwasserbohrung mit geringer Schüttung. Der Mineralbrunnen, 10/97, 458-466.

Rummel F, Hansen J (1989): Interpretation of hydrofrac pressure recordings using a simple fracture mechanics simulation model. Int. J. Rock Mech., 26/6, 483-488.

Sneddon IN (1946): The distribution of stress in the neighbourhood of a crack in an elastic solid. Proc. Roy. Sic. London, A 187, 229-260.

Zoback MD, Harjes HP (1997): Injection induced earthquakes and crustal stress at 9 km depth at the KTB deep drilling site, Germany. JGR, 105/B8, 18477-18491.